## Slide 2
Add IP : ZYNQ7 Processing System
Click Run Block Automation

## Slide 3
Add IP: gpio
Click Run Connection Automation

## Slide 5
Click Run Connection Automation

## Slide 6
Select Board Part Interface : leds_4bits(LED)

## Slide 7
Add IP: AXI Timer
Click Run Connection Automation

## Slide 9
Click processing_system7_0 block
Interrupts IRQ_F2P

## Slide 10
Connect axi_timer interrupt to processing_system7 IRQ_F2P

## Slide 11
Click validate design
Sources
Create HDL Wrapper

## Slide 13
Generate Bitstream
Click save

## Slide 14
Click ok

## Slide 16
File >> Export>> Export Hardware
Click ok

## Slide 17
File>>Launch SDK

## Slide 18: Timer_LED

## Slide 19
Select “Hello World”